## Slide 1: Chapter 9- Bit Operations (part 1): Shift Operations
Jihene Kaabi & Youssef Harrath

## Slide 2: Shift Instructions
Pentium provides two types of shift instructions: one type for performing logical shifts, and the other for performing arithmetic shifts.
The logical shift instructions are:
  shl (SHift Left)
  shr (SHift Right)
The arithmetic shift instructions are
  sal (Shift Arithmetic Left)
  sar (Shift Arithmetic Right)
The logical shift instructions work on unsigned binary numbers, and the arithmetic shift instructions work on signed binary numbers.

## Slide 3: Logical Shift Instructions
The logical shift instructions have the following general format:
  shl destination, count
  shr destination, count
The destination can be an 8-, 16- or 32-bit operand stored either in a register or in memory.
The second operand specifies the number of bit positions to be shifted.
The destination is shifted left or right by count bit positions.

## Slide 4: Logical Left Shift Instruction
The shl instruction can be used to left shift a destination operand.
Each bit shift to the left causes the leftmost bit to move to the carry flag (CF), and the vacated rightmost bit is filled with a 0 bit.
The bit that was in CF is lost as a result of the left shift operation.

## Slide 5: Logical Right Shift Instruction
The shr instruction works similarly but shifts bits to the right.
There are two versions of each instruction depending on how the count value is specified. The count can be given as an immediate value or in the CL register. Thus, the formats of these instructions are,
  shl destination, count shr destination, count
  shl destination,CL shr destination,CL
The first format can be used to specify directly the number of bit positions to be shifted. The value of count can range from 0 to 31.
The second format can be used to indirectly specify the shift count, which is assumed to be in the CL register. The CL register contents are not changed by the shl and shr instructions.
The CL versions are useful when we don't know the count value (e.g., given as a parameter in a procedure call). In general, the first format is faster.

## Slide 6: Logical Shifts (Examples)
Here are some code examples:
mov ax, 0C123h
shl ax, 1 ; shift 1 bit to left, ax = ???, CF = ???
After 1 left shift
ax = 8246h, CF = 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0

## Slide 7: Exercise: Logical Shifts:
Evaluate the values of ax and CF after each of the following logical shifts.
mov ax, 8246h
shr ax, 1 ax = ??, CF = ??
shr ax, 1 ax = ??, CF = ??
Notes: AX = 4123 h , CF = 0
AX = 2091 h , CF = 1

## Slide 8: Exercise: Logical Shifts: (Solution)
Evaluate the values of ax and CF after each of the following logical shifts.
mov ax, 8246h
shr ax, 1 ax = 4123h, CF = 0
shr ax, 1 ax = 2091, CF = 1
Notes: AX = 4123 h , CF = 0
AX = 2091 h , CF = 1

## Slide 9: Use of Logical Shifts
The common use for shifts: quickly multiply and divide by powers of 2.
In decimal, for instance:
  multiplying 0013 by 10 amounts to doing one left shift to obtain 0130
  multiplying 0013 by 100=102 amounts to doing two left shifts to obtain 1300
In binary
  multiplying 00101 by 2 amounts to doing a left shift to obtain 01010
  multiplying 00101 by 4=22 amounts to doing two left shifts to obtain 10100

## Slide 10: Use of Logical Shifts (cont.)
If numbers are too large, then we’d need more bits and multiplication doesn’t produce valid results.
  e.g., 10000000 (128d) cannot be left-shifted to obtain 256 using 8-bit values.
Similarly, dividing by powers of two amounts to doing right shifts:
  right shifting 10010 (18d) leads to 01001 (9d)

## Slide 11: Use of Logical Shifts (odd numbers)
Note that when dividing odd numbers by two we “lose bits”, which amounts to rounding to the lower integer quotient.
Consider number 10011 (19d)
  Right shift: 01001 (9d: 19/2 rounded below)
  Right shift: 00100 (4d: 9/2 rounded below)

## Slide 12: Logical Shifts and Unsigned Numbers
Using shifts works only for unsigned numbers
When numbers are signed, the shifts do not handle the sign bits correctly and cannot be interpreted as multiplying/dividing by powers of 2 anymore.
Example: Consider the 1-byte number FE
  If unsigned
    FE = 254d = 11111110b
    Right shift: 01111111b = 7Fh = 127d = (254/2)
  If signed
    FE = -2d = 11111110b
    Right shift: 01111111b = 7Fh = +127d (which is not -2/2)

## Slide 13: Arithmetic Shifts
Since the logical shifts do not work for signed numbers, we have another kind of shifts called arithmetic shifts.
Left arithmetic shift: sal
  This instruction works just like shl
    We just have another name for it so that in the code we “remember” that we’re dealing with signed numbers
  As long as the sign bit is not changed by the shift, the result will be correct (i.e., will be multiplied by 2).

## Slide 14: Arithmetic Shifts (cont.)
Right arithmetic shift: sar
  This instruction does NOT shift the sign bit.
  The other bits are shifted as normal except that the new bits that enter from the left are copies of the sign bit (that is, if the sign bit is 1, the new bits are also 1).
Thus, if a byte is shifted with this instruction, only the lower 7 bits are shifted.
Both shifts store the last bit out in the carry flag

## Slide 15: Arithmetic Shifts Examples
If signed numbers, then the operations below are correct multiplications /divisions of 1-byte quantities.
mov al, 0C3h ; al = 11000011 (-61d)
sal al, 1 ; al = 10000110 (86h = -122d)
sar al, 3 ; al = 11000011 (after the 1st shift)
; al = 11100001 (after the 2nd shift)
; al = 11110000 (after the 3rd shift (F0h = -16h))
; (note that this is not an exact division as we lose bits on ; the right!)
The following is not a correct multiplication by 16! sal al, 4 ; al = 0000 0000 (0d, which can’t be right)

## Slide 16: Doubling of Signed Numbers
Perform successive multiplications by powers of 2 and fill in the following table.
Instruction | Signed Binary Number (al) | Decimal Value
 | 00001011 | +11
sal al, 1 |  | 
sal al, 2 |  | 
sal al, 3 |  | 
 | 11110101 | -11
sal al, 1 |  | 
sal al, 2 |  | 
sal al, 3 |  | 

## Slide 17: Doubling of Signed Numbers (Solution)
Perform successive multiplications by powers of 2 and fill in the following table.
Instruction | Signed Binary Number (al) | Decimal Value
 | 00001011 | +11
sal al, 1 | 00010110 | +22
sal al, 2 | 00101100 | +44
sal al, 3 | 01011000 | +88
 | 11110101 | -11
sal al, 1 | 11101010 | -22
sal al, 2 | 11010100 | -44
sal al, 3 | 10101000 | -88

## Slide 18: Halving of Signed Numbers
Perform successive divisions by powers of 2 and fill in the following table.
Instruction | Signed Binary Number (al) | Decimal Value
 | 01011000 | +88
sar al, 1 |  | 
sar al, 2 |  | 
sar al, 3 |  | 
 | 10101000 | -88
sar al, 1 |  | 
sar al, 2 |  | 
sar al, 3 |  | 

## Slide 19: Halving of Signed Numbers (Solution)
Perform successive divisions by powers of 2 and fill in the following table.
Instruction | Signed Binary Number (al) | Decimal Value
 | 01011000 | +88
sar al, 1 | 00101100 | +44
sar al, 2 | 00010110 | +22
sar al, 3 | 00001011 | +11
 | 10101000 | -88
sar al, 1 | 11010100 | -44
sar al, 2 | 11101010 | -22
sar al, 3 | 11110101 | -11

## Slide 20: Rotate Shifts
The rotate shift instructions work like logical shifts except that bits lost off one end of the data are shifted in on the other side.
  Thus, the data is treated as if it is a circular structure.
The two simplest rotate instructions are ROL and ROR which make left and right rotations, respectively.
Just as for the other shifts, these shifts leave a copy of the last bit shifted around in the carry fag.

## Slide 21: Rotate Shifts (Examples)
mov ax, 0C123h (1100000100100011b)
  rol ax, 1
  rol ax, 1
  rol ax, 1
  ror ax, 2
  ror ax, 1
  ; ax = 8247h, CF = 1
  ; ax = 048Fh, CF = 1
  ; ax = 091Eh, CF = 0
  ; ax = 8247h, CF = 1
  ; ax = C123h, CF = 1
1100000100100011
x
1
1000001001000111
x
1
0000010010001111
x
0
0000100100011110
x
0
0000010010001111
x
1
1000001001000111
x
1

## Slide 22: Rotate through Carry Shifts
There are two additional rotate instructions that shift the bits in the data and the carry flag named RCL and RCR.
The Instruction RCL (Rotate through Carry Left) shifts the bits of the destination to the left. The msb is shifted Into the CF, and the previous value of CF is shifted Into the rightmost bit.
RCL works like just like ROL, except that CF is part of the circle of bits being rotated. The syntax is similar to ROL.

## Slide 23: Rotate Shifts: Example
For example, if the AX register is rotated with these instructions, the 17-bits made up of AX and the carry flag are rotated.
mov ax, 0C123h
clc ; clear the carry flag (CF = 0)
rcl ax, 1
So, ax = 8246h and CF =1
1 1 0 0 0 0 0 1 0 0 1 0 0 0 1 1 0
x
0
CF =0

## Slide 24: Rotate Shifts: Exercise
mov ax, 8246h, CF =1
rcl ax, 1 ; ax = ??, CF = ??
rcl ax, 1 ; ax = ??, CF = ??
rcr ax, 2 ; ax = ??, CF = ??
rcr ax 1 ; ax = ??, CF = ??

## Slide 25: Rotate Shifts: Exercise (Solution)
mov ax, 8246h, CF =1
rcl ax, 1 ; ax = 048Dh, CF = 1
rcl ax, 1 ; ax = 091Bh, CF = 0
rcr ax, 2 ; ax = 8246h, CF = 1
rcr ax, 1 ; ax = C123h, CF = 0