## Slide 1: Chapter 2- Computer Organization
Jihene Kaabi & Youssef Harrath

## Slide 2: Memory
The basic unit of memory is byte.
  A computer with 32 megabytes of memory can hold roughly 32 millions of information.
Each byte in memory is labeled by a unique number known as its address.

## Slide 3: Memory (cont.)
Often memory is used in larger chunks than single bytes.
On the PC architecture, names have been given to these larger sections of memory as shown below.

## Slide 4: Memory (cont.)
All data in memory is numeric.
Characters are stored by using a character code that maps numbers to characters.
  One of the most common character codes is known as ASCII (American Standard Code for Information Interchange).
  A new, more complete code that is replacing ASCII is Unicode.
  One key difference between the two codes is that ASCII uses one byte to encode a character, but Unicode uses multiple bytes.

## Slide 5: The CPU
The Central Processing Unit (CPU) is the physical device that performs instructions.
The instructions that CPUs perform are generally very simple.
  Instructions may require the data they act on to be in special storage locations in the CPU itself called registers.
The CPU can access data in registers much faster than data in memory.

## Slide 6: The CPU: Machine Language
The instructions a type of CPU executes make up the CPU’s machine language.
Machine programs have a much more basic structure than higher-level languages.
Machine language instructions are encoded as raw numbers, not in friendly text formats.
A CPU must be able to decode an instruction’s purpose very quickly to run efficiently.

## Slide 7: The CPU
Programs written in other languages must be converted to the native machine language of the CPU to run on the computer.
A compiler is a program that translates programs written in a programming language into the machine language of a particular computer architecture.
In general, every type of CPU has its own unique machine language.
  This is one reason why programs written for a Mac cannot run on an IBM-type PC.

## Slide 8: Processor Operating Modes
Real mode: A program may access any memory address, even the memory of other programs.
  This makes debugging and security very difficult
16-bit Protected mode: This mode allows access to up to 16 megabytes of addressable memory. It prevents programs from accessing each other’s memory.
32-bit Protected mode: This mode allows access to up to 4 gigabytes of addressable memory.

## Slide 9: The 80x86 family of CPU
8088, 8086 Used in the earliest PC’s. Provide several 16-bit registers (AX, BX, CX, …) Only support up to 1 megabyte of memory and only operate in real mode. Programs are divided into segments not larger than 64K each. | 80286 Was used in AT class PC’s. Adds some new instructions to the base machine language of 808886. Its main new feature is 16-bit protected mode. Programs are still divided into segments that could not be bigger than 64K.
80386 Greatly enhanced the 80286 Extends many of the registers to hold 32-bits. Adds two new 16-bit registers FS and GS. Adds a new 32-bit protected mode Programs are again divided into segments that can be up to 4 gigabytes in size. | 80486 / Pentium / Pentium Pro Add very few features They mainly speed up the execution of the instructions.

## Slide 10: The 80x86 family of CPU (cont.)
Pentium MMX Adds the MMX (MultiMedia eXtensions) instructions to the Pentium. These instructions can speed up common graphics operations. | Pentium II - This is the Pentium Pro processor with the MMX instructions added. (The Pentium III is essentially just a faster Pentium II.)

## Slide 11: 8086 16-bit Registers: General purpose registers
The original 8086 CPU provided four 16-bit general purpose registers: AX, BX, CX and DX.
Each of these registers could be decomposed into two 8-bit registers.
  For example, the AX register could be decomposed into the AH and AL registers as shown below.
  The AH register contains the upper (or high) 8 bits of AX and AL contains the lower 8 bits of AX.
They are used in many of the data movement and arithmetic instructions.

## Slide 12: 8086 16-bit Registers
16-bit BP and SP registers: used to point to data in the machine language stack and are called the Base Pointer and Stack Pointer, respectively.
16-bit CS, DS, SS and ES registers: are segment registers.
  They denote what memory is used for different parts of a program.
  CS stands for Code Segment, DS for Data Segment, SS for Stack Segment and ES for Extra Segment.
  ES is used as a temporary segment register.

## Slide 13: 8086 16-bit Registers
Instruction Pointer (IP) register: used with the CS register to keep track of the address of the next instruction to be executed by the CPU.
  Normally, as an instruction is executed, IP is advanced to point to the next instruction in memory.
The FLAGS register: stores important information about the results of a previous instruction.
  These results are stored as individual bits in the register.
  For example, the Z bit is 1 if the result of the previous instruction was zero or 0 if not zero.

## Slide 14: 80386 32-bit Registers
The 80386 and later processors have extended registers.
  For example, the 16-bit AX register is extended to be 32-bits.
To be backward compatible, AX still refers to the 16-bit register and EAX is used to refer to the extended 32-bit register.
AX is the lower 16-bits of EAX just as AL is the lower 8- bits of AX (and EAX).
There is no way to access the upper 16-bits of EAX directly.

## Slide 15: 80386 32-bit Registers (cont.)
The other extended registers are EBX, ECX, EDX, ESI and EDI.
Many of the other registers are extended as well.
  BP becomes EBP; SP becomes ESP; FLAGS becomes EFLAGS and IP becomes EIP.
  Unlike the index and general-purpose registers, in 32-bit protected mode only the extended versions of these registers are used.
The segment registers are still 16-bit in the 80386.
There are also two new segment registers: FS and GS.

## Slide 16: Real Mode
Memory is limited to only one megabyte (220 bytes).
Valid address range from (in hex) 00000 to FFFFF.
  These addresses require a 20-bit number.
  Obviously, a 20-bit number will not fit into any of the 8086’s 16-bit registers.
  Intel solved this problem, by using two 16-bit values to determine an address.

## Slide 17: Real Mode (cont.)
The first 16-bit value is called the selector. Selector values must be stored in segment registers.
The second 16-bit value is called the offset.
The physical address referenced by a 32-bit selector:offset pair is computed by the formula
16 ∗ selector + offset
Multiplying by 16 in hex is easy, just add a 0 to the right of the number.

## Slide 18: Real Mode: translation from logical to physical address
Append four least significant zeros to the segment base address
  Just add a zero when using hex numbers
Add the offset value
Example: Translate logical address 1100:450
11000 (add zero to segment address)
450 (offset value)
11450 (20-bit physical address)

## Slide 19: Translation from logical to physical address:
Question:
Translate logical address 047C:0048
Answer:
0 4 7 C 0 (add zero to segment address)
0 0 4 8 (offset value)
0 4 8 0 8 (20-bit physical address)

## Slide 20: Real Mode: Disadvantage
A single selector value can only reference 64K of memory (the upper limit of the 16-bit offset).
What if a program has more than 64K of code?
  A single value in CS cannot be used for the entire execution of the program.
  The program must be split up into sections (called segments) less than 64K in size.
  When execution moves from one segment to another, the value of CS must be changed.

## Slide 21: Real Mode: Disadvantage (cont.)
Each byte in memory does not have a unique segmented address.
The physical address 04808 can be referenced by 047C:0048, 047D:0038, 047E:0028 or 047B:0058.
This can complicate the comparison of segmented addresses.

## Slide 22: The 80286 16-bit Protected Mode
Selector values are interpreted completely differently than in real mode.
In real mode, a selector value is a paragraph number of physical memory.
In protected mode, a selector value is an index into a descriptor table.

## Slide 23: The 80286 16-bit protected Mode (cont.)
In both modes, programs are divided into segments.
  In real mode, these segments are at fixed positions in physical memory and the selector value denotes the paragraph number (16 bytes) of the beginning of the segment.
  In protected mode, the segments are not at fixed positions in physical memory.

## Slide 24: The 80286 16-bit protected Mode (cont..)
It uses a technique called virtual memory (VM).
The basic idea of a VM system is to only keep the data and code in memory that programs are currently using.
  Other data and code are stored temporarily on disk until they are needed again.
Segments are moved between memory and disk as needed.
When a segment is returned to memory, it will be put into a different area of memory that it was in before being moved to disk.
  All of this is done transparently by the operating system.
  The program does not have to be written differently for virtual memory to work.

## Slide 25: The 80286 16-bit protected Mode (cont…)
In protected mode, each segment is assigned an entry in a descriptor table.
This entry has all the information that the system needs to know about the segment.
This information includes: is it currently in memory; if in memory, where is it; access permissions (e.g., read-only).
The index of the entry of the segment is the selector value that is stored in segment registers.

## Slide 26: The 80286 16-bit protected Mode (cont.)
One big disadvantage of 16-bit protected mode is that offsets are still one 16-bit quantities.
Because of this, segment sizes are still limited to at most 64K.
  This makes the use of large arrays problematic!

## Slide 27: The 80386 32-bit Protected Mode
There are two major differences between 386 32-bit and 286 16-bit protected modes:
Offsets are expanded to be 32-bits.
  This allows an offset to range up to 4 billion.
  Thus, segments can have sizes up to 4 gigabytes.

## Slide 28: The 80386 32-bit Protected Mode
Segments can be divided into smaller 4K-sized units called pages.
The virtual memory system works with pages now instead of segments.
This means that only parts of segment may be in memory at any one time.
In 286 16-bit mode, either the entire segment is in memory or none of it is.
This is not practical with the larger segments that 32-bit mode allows.

## Slide 29: Interrupts
Sometimes the ordinary flow of a program must be interrupted to process events that require prompt response.
The hardware of a computer provides a mechanism called interrupts to handle events that require prompt response.
  For example, when a mouse is moved, the mouse hardware interrupts the current program to handle the mouse movement (to move the mouse cursor, etc.)
Interrupts cause control to be passed to an interrupt handler.
Interrupt handlers are routines that process the interrupt.

## Slide 30: Interrupts (cont.)
Many interrupt handlers return control back to the interrupted program when they finish.
They restore all the registers to the same values they had before the interrupt occurred.
Thus, the interrupted program runs as if nothing happened (except that it lost some CPU cycles).